## Slide 1: Introduction to Parallelism
Lecture 10
Hartmut Kaiser
https://teaching.hkaiser.org/spring2025/csc4700/

## Slide 2: Multicore for HPC
How do multicore chips operate (how does the hardware work)?
How do they get high performance?
How does the software exploit the hardware (how do we write our software to exploit the hardware)?
What are the abstractions that we need to use to reason about multicore systems?
What are the programming abstractions and mechanisms?
Terminology: Program, process, thread
More terminology: Parallel, concurrent, asynchronous

## Slide 3: Multicore Architecture
Any CPU in the last 4-5 years
Core is a FDREW + regs
Each runs its own sequence of instructions
Each can access its own data
But memory might be shared
Each has memory hierarchy

## Slide 4: Parallelism and Concurrency
Parallelism may be defined as performing two (or more) activities at the same time
  These activities may be related in some manner or not
  Usually, these activities are not instantaneous: each takes a finite time
Two related activities are said to be concurrent if there is no predetermined order between them
  They may or may not overlap in time when they do occur
In certain situations, concurrency is not desirable and a relative order is imposed
  When such an order is enforced on two activities, they clearly cannot be executed in parallel

## Slide 5: Why Parallelism?
Natural processes are inherently parallel, whether they be molecular and nuclear behavior, weather and geological phenomena, or biological and genetic manifestation
Modelling such processes require highly complex computations
  For example, a nanosecond-long molecular dynamics simulation of barely a million atoms can take more than 1017 steps (a billion billion steps)
  Highly detailed week-long weather modeling requires even higher orders of magnitude
Modern CPUs are able to complete ‘only’ a few billion sequential steps in a second
Without parallelism, many useful computations would literally take a lifetime

## Slide 6: Sequential Computation
Traditionally software has been written for sequential computations
  To be run on a single computer having a single Central Processing Unit (CPU)
A problem is broken into a discrete set of instructions
Instructions are executed one after another
Only one instruction can be executed at any moment in time

## Slide 7: Parallel Computing
In the simplest sense, parallel computing is the simultaneous use of multiple compute resources to solve a computational problem
  To be run using multiple CPUs concurrently
A problem is broken into discrete parts that can be solved concurrently
Each part is further broken down to a series of instructions
Instructions from each part execute simultaneously on different CPUs

## Slide 8: Parallel Computers
Virtually all stand-alone computers today are parallel from a hardware perspective
  Multiple functional units (floating point, integer, GPU, etc.)
  Multiple execution units / cores
  Multiple hardware threads
Intel Core i7 CPU and its major components

## Slide 9: Parallel Computers (HPC)
Networks connect multiple stand-alone computers (nodes) to create larger parallel computer clusters
Each compute node is a multi-processor parallel computer in itself
Multiple compute nodes are networked together with a high-bandwidth, low-latency network (e.g., InfiniBand )
Special purpose nodes, also multi-processor, are used for other purposes

## Slide 10: Why Use HPC?
Major reasons
Save time and/or money: In theory, throwing more resources at a task will shorten its time to completion, with potential cost savings. Parallel clusters can be built from cheap, commodity components
Solve larger problems: Many problems are so large and/or complex that it is impractical or impossible to solve them on a single computer, especially given limited computer memory
Provide concurrency: A single compute resource can only do one thing at a time. Multiple computing resources can be doing many things simultaneously
Use of non-local resources: Using compute resources on a wide area network, or even the Internet when local compute resources are scarce

## Slide 11: Future Trends
Source: Top500.org

## Slide 12: HPC Terminology
Supercomputing / High-Performance Computing (HPC)
Flop/s – Floating point operation per second
Node – a stand alone computer
CPU / Core – a modern CPU usually has several cores (individual processing units)
Task – a logically discrete section from the computational work
Communication – data exchange between parallel tasks
Speedup – time of serial execution / time of parallel execution
Massively Parallel – refer to hardware of parallel systems with many processors (“many” = hundreds of thousands)
Embarrassingly Parallel – solving many similar but independent tasks simultaneously. Requires very little communication
Scalability – a proportionate increase in parallel speedup with the addition of more processors

## Slide 13: Parallel Computer Memory Architectures
Shared Memory
Multiple processors can operate independently, but share the same memory resources
Changes in a memory location caused by one CPU are visible to all processors
Advantages
Global address space provides a user-friendly programming perspective to memory
Fast and uniform data sharing due to proximity of memory to CPUs
Disadvantages
Lack of scalability between memory and CPUs. Adding more CPUs increases traffic on the shared memory-CPU path
Programmer responsibility for “correct” access to shared memory

## Slide 14: Parallel Computer Memory Architectures
Distributed Memory
Requires a communication network to connect inter-processor memory
Processors have their own local memory. Changes made by one CPU have no effect on others
Requires communication to exchange data among processors
Advantages:
Memory is scalable with the number of CPUs
Each CPU can rapidly access its own memory without overhead incurred by trying to maintain global cache coherency
Disadvantages:
Programmer is responsible for many of the details associated with data communication between processors
It is usually difficult to map existing data structures to this memory organization, based on global memory

## Slide 15: Parallel Computer Memory Architectures
Hybrid Distributed-Shared Memory
The largest and fastest computers in the world today employ both shared and distributed memory architectures.
Shared memory component can be a shared memory machine and/or GPU
Processors on a compute node share same memory space
Requires communication to exchange data between compute nodes
Advantages and Disadvantages
Whatever is common to both shared and distributed memory architectures
Increased scalability is an important advantage
Increased programming complexity is a major disadvantage
15

## Slide 16: Parallel Programming Models

## Slide 17: Parallel Programming Models
Parallel Programming Models exist as an abstraction on top of hardware and memory architectures
Uniform Memory (without threads)
Shared Threads Models (Pthreads, OpenMP, HPX)
GPU programming (CUDA, HIP, SYCL, etc.)
Distributed Memory (HPX) / Message Passing (MPI)
Data Parallel (HPX)
Hybrid (HPX, MPI+OpenMP)
Single Program Multiple Data (SPMD)
Multiple Program Multiple Data (MPMD)

## Slide 18: Shared Threads Models
POSIX Threads
  Library based, requires parallel coding
  C Language only; Interfaces for Perl, Python and others exist
  Commonly referred to as Pthreads
  Most hardware vendors now offer Pthreads in addition to their proprietary threads implementations
  Very explicit parallelism; requires significant programmer attention to detail
OpenMP
  Compiler directive based (#pragma directives); can use serial code
  Jointly defined and endorsed by a group of major computer hardware and software vendors
  Portable / multi-platform, including Unix and Windows platforms
  Available in C/C++ and Fortran implementations
  Can be very easy and simple to use - provides for "incremental” parallelism

## Slide 19: Shared Threads Models
Pthreads are the underlying threading implementation on almost all platforms
  Too low level for daily use
OpenMP does not integrate with C++ very well
  Is based on #pragma’s that don’t know anything about C++ types
  Very verbose if fine tuning is needed
We will use higher level standard C++ facilities
  Later we will use HPX, which provides extensions to the standard C++ APIs

## Slide 20: Distributed Memory / Message Passing Models
A set of processes that use their own local memory during computation
  Multiple tasks can reside on the same physical machine and/or across an arbitrary number of machines
Processes exchange data through communications by sending and receiving messages
Data transfer usually requires cooperative operations to be performed by each process
  For example, a send operation must have a matching receive operation
Message Passing Interface (MPI) is the "de facto" industry standard for message passing
  MPI implementations exist for virtually all popular parallel computing platforms
Distributed task-based systems like HPX combine benefits of both, one sided and tw0-sided communication

## Slide 21: Data Parallel Model
Data Parallel on shared memory systems
  SIMD registers and arithmetic operations
Is applicable semantically to distributed computing as well (SPMD/MPMD)
  Relies on systems that expose a Global Address Space
  UPC/UPC++: Partitioned Global Address Space (PGAS) (compiler dependent)
  Coarray Fortran: A small set of extension to Fortran 95 (compiler dependent)
  HPX: Active Global Address Space (AGAS) (pure library implementation)
Display these characteristics:
  Address space is treated globally
  Parallel work focuses on performing operations on a data set
  Tasks work on different portions from the same data structure
  Tasks may perform different operations concurrently
19

## Slide 22: Hybrid Parallel Programming Models
Currently, a common example of a hybrid model is the combination of the message passing model (MPI) with the threads model (OpenMP)
  Threads perform computationally intensive kernels using local, on-node data
  Communications between processes on different nodes occurs over the network using MPI
This hybrid model lends itself well to the increasingly common hardware environment of clustered multi/many-core machines
HPX: a C++ library solution combining
  Distributed tasks
  Seamless local threading
  Higher-level APIs uniform for local and remote operation

## Slide 23: Hybrid Parallel Programming Models:
Another similar and increasingly popular example of a hybrid model is using MPI with GPU (Graphics Processing Unit) programming
  GPUs perform computationally intensive kernels using local, on-node data
  Communications between processes on different nodes occurs over the network using MPI
HPX allows to unify the programming interfaces for
  Shared memory parallelism
  Distributed parallelism
  GPU based computation

## Slide 24: Can my Code be parallelized?
Does it have large loops that repeat the same operations?
Does your code do multiple tasks that are not dependent on one another? If there are dependencies, are those weak?
Can any dependencies or information sharing be overlapped with computation? If not, is the amount of communications small?
Do multiple tasks depend on the same data?
Does the order of operations matter? If so how strict does it have to be?

## Slide 25: Basic Guidance for efficient Parallelization
Is it even worth parallelizing my code?
  Does your code take an intractably long amount of time to complete?
  Do you run a single large model or do statistics on multiple small runs?
Would the amount of time it takes to parallelize your code be worth the gain in speed?
  Parallelizing established code vs. starting from scratch
  Established code: Maybe easier / faster to parallelize, but may not give good performance or scaling
  Start from scratch: Takes longer, but will give better performance, accuracy, and gives the opportunity to turn a “black box” into a code you understand

## Slide 26: Basic Guidance for efficient Parallelization
Increase the fraction of your program that can be parallelized
  Identify the most time consuming parts of your program and parallelize them
  This could require modifying your intrinsic algorithm and code’s organization
Balance parallel workload
Minimize time spent in communication
Partition data. Distribute arrays and matrices – allocate specific memory for each process on a separate node

## Slide 27: Considerations about Parallelization
You parallelize your program to run faster, and to solve larger and more complex problems
  How much faster will the program run?
  : Time to complete the job on one process
  : Time to complete the job on n processes
T (n)
T (1)
S(n) 
Speedup:
Efficiency:
n
E(n)  S(n)
Tells you how efficiently you parallelize your code

## Slide 28: Oversimplified Example
fraction of program that can be parallelized
  fraction of program that cannot be parallelized
number of processors
Then the time of running the parallel program will be of the time for running the serial program
  Example: if 80% can be parallelized and 20 % cannot be parallelized
    i.e., 40% of the time for running the serial code
You get 2.5 speed up although you run on 4 cores since only 80% of your code can be parallelized (assuming that all parts in the code can complete in equal time)

## Slide 29: Oversimplified Example, continued
20%
80%
Parallel
Process 1
Process 2
Process 3
parallelized
Not parallelized
Process 4
Serial

## Slide 30: More realistic Example
20%
80%
Parallel
Process 1
Process 2
Process 3
parallelized
Not parallelized
Process 4
Serial
Overheads
Load imbalance

## Slide 31: Designing parallel Programs - Partitioning
One of the first steps in designing a parallel program is to break the problem into discrete “chunks” that can be distributed to multiple parallel tasks
Domain Decomposition
  Data associated with a problem is partitioned
  Each parallel task works on a portion of the data
There are different ways to partition the data

## Slide 32: Designing parallel Programs - Partitioning
One of the first steps in designing a parallel program is to break the problem into discrete “chunks” that can be distributed to multiple parallel tasks
Functional Decomposition
  Problem is decomposed according to the work that must be done. Each parallel task performs a fraction of the total computation

## Slide 33: Designing parallel Programs - Communication
Most parallel applications require tasks to share data with each other
Cost of communication: Computational resources are used to package and transmit data
  Requires frequently synchronization – some tasks will wait instead of doing work
  Could saturate network bandwidth
Latency vs. Bandwidth
  Latency is the time it takes to send a minimal message between two tasks
  Bandwidth is the amount of data that can be communicated per unit of time
  Sending many small messages can cause latency to dominate communication overhead

## Slide 34: Designing parallel Programs - Communication
Most parallel applications require tasks to share data with each other
Synchronous vs. Asynchronous communication
  Synchronous communication is referred to as blocking communication – other work stops until the communication is completed
  Asynchronous communication is referred to as non-blocking since other work can be done while communication is taking place

## Slide 35: Designing parallel Programs - Communication
Most parallel applications require tasks to share data with each other
Scope of communication
  Point-to-point communication – data transmission between tasks.
Collective communication
  Involves all tasks (in a communication group)

## Slide 36: Designing parallel Programs - Load Balancing
Load balancing is the practice of distributing approximately equal amount of work so that all compute resources are kept busy all the time
How to Achieve Load Balance?
Equally partition the work given to each task
  For array/matrix operations equally distribute the data set among parallel tasks
  For loop iterations where the work done for each iteration is equal, evenly distribute iterations among tasks
Use dynamic work assignment
  Certain class problems result in load imbalance even if data is distributed evenly among tasks (sparse matrices, adaptive grid methods, many body simulations, etc.).
  Use scheduler – task pool approach. As each task finishes, it queues to get a new piece of work. Modify your algorithm to handle imbalances dynamically.

## Slide 37: Scalability

## Slide 38: Name This Famous Person
"Validity of the single processor approach to achieving large-scale computing capabilities,” AFIPS Conference Proceedings (30): 483–485, 1967.
Gene Amdahl (1922-2015)
Amdahl’s Law
Notes: Michael Flynn, "Very high-speed computing systems," Proceedings of the IEEE , vol.54, no.12, pp.1901,1909, Dec. 1966.
Gene Amdahl, "Validity of the single processor approach to achieving large-scale computing capabilities,” AFIPS Conference Proceedings (30): 483–485, 1967.

## Slide 39: Amdahl’s Law
Serial time on 1 processor:
Parallel time on processors:
Parallel overhead:
Best case:
: Proportion of parallel code

## Slide 40: Amdahl’s Law (Strong Scaling)
: Speedup
: Proportion of parallel code
: Number of processors
Figure courtesy of Wikipedia (http://en.wikipedia.org/wiki/Amdahl's_law)

## Slide 41: A simple Example
Consider a two-step computation on a N x N image
  Step 1: multiply brightness of all pixels by two (independent computation on each pixel)
  Step 2: compute average of all pixel values
Sequential implementation of program
  Both steps take ~ N2 time, so total time is ~ 2N2
N
N
Execution time
Parallelism
N2
N2
1

## Slide 42: First attempt at Parallelism (P Processors)
Strategy:
  Step 1: execute in parallel
    time for phase 1:
  Step 2: execute sequentially
    time for phase 2:
Overall performance:
  Speedup
  Speedup ≤ 2
Execution time
Parallelism
N2
N2/P
P
1
Execution time
Parallelism
N2
N2
1
P
Sequential program
Parallel program

## Slide 43: Parallelizing Step 2
Strategy:
  Step 1: execute in parallel
    time for phase 1:
  Step 2: compute partial sums in parallel, combine results sequentially
    time for phase 2:
Overall performance:
Speedup
Execution time
Parallelism
N2/P
Note: speedup → P when N >> P
1
P
Overhead of parallel algorithm: combining the partial sums
Parallel program
N2/P P

## Slide 44: Amdahl’s Law
A small serial region can limit speedup on a large parallel machine
  Summit supercomputer:
    27,648 GPUs x (5,376 ALUs/GPU) = 148,635,648 ALUs
    Machine can perform 148 million single precision operations in parallel
  What is max speedup if 0.1% of application is serial?

## Slide 45: Rule 1
Parallelize Applications as Much as Humanly Possible

## Slide 46
The 4 Horsemen of the Apocalypse

## Slide 47
Starvation
  Insufficient concurrent work to maintain high utilization of resources
Latencies
  Time-distance delay of remote resource access and services
Overheads
  Work for management of parallel actions and resources on critical path which are not necessary in sequential variant
Waiting for Contention resolution
  Delays due to lack of availability of oversubscribed shared resources
Additional Factors that limit Scalability

## Slide 48: Universal Scalability Law
λ: Scaling efficiency
δ: Contention
κ: Latencies (‘Crosstalk’)
N: Number of processors

## Slide 49: Real-world Problems
Even standard algorithms added to C++17 enforce fork-join semantics

## Slide 50: Fork/Join Parallelism

## Slide 51: Rule 2
Use a Programming Environment that Embraces SLOW

## Slide 52: Name This Famous Person
"Reevaluating Amdahl's Law". Communications of the ACM. 31 (5): 532–3, May 1988
Recipient of the inaugural Gordon Bell Prize in 1998
John Gustafson
Gustafson’s Law

## Slide 53: Oversimplified Example, again:
parallelized
Not parallelized
Serial
Parallel
Process 1
Process 2
Process 3
Process 4
: Time spent running parallel code

## Slide 54: Gustafson’s Law (Weak Scaling)
Doing the same problem faster and faster is not how we use parallel computers
  Rather, we solve bigger and more difficult problems
  I.e., the amount of parallelizable work grows
: Speedup
: Portion of parallelized code
N: Number of processors

## Slide 55: Parallel Scaling & Efficiency
Two kinds of scaling used:
Strong scaling: fixed problem size
  , sometimes calculated as
  Ideally scales linearly, sometimes super-linearly
  Parallel efficiency: (in %)
Weak scaling: problem size proportional to
  Keeps effective problem size per processor constant
  Ideally a flat line close to 1
  Parallel efficiency:

## Slide 56: Overheads: Thought-Experiment
Chart: Execution Time over Grain Size (for different amounts of overheads per thread, 16 Cores)
| 1 | 2 | 10 | 20 | 100 | 200 | 1000 | 2000 | 10000 | 20000 | 100000 | 200000 | 1000000 | 2000000 | 10000000
Sequential Time | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1µs Overhead | 10.1009 | 5.1009 | 1.1009 | 0.6009 | 0.20091 | 0.15091 | 0.11095 | 0.106 | 0.1024 | 0.1024 | 0.106 | 0.11095 | 0.25091 | 0.65091 | 1.5009
100µs Overhead | 1000.1009 | 500.1009 | 100.1009 | 50.1009 | 10.1009 | 5.1009 | 1.101 | 0.601 | 0.2014 | 0.1519 | 0.1159 | 0.1159 | 0.2519 | 0.6514 | 1.501
10ms Overhead | 100000.1009 | 50000.1009 | 10000.1009 | 5000.1009 | 1000.1009 | 500.1009 | 100.1009 | 50.101 | 10.1014 | 5.1019 | 1.1059 | 0.6109 | 0.3509 | 0.7009 | 1.5109

## Slide 57: Overheads: The Worst of All?
Even relatively small amounts of work can benefit from being split into smaller tasks
  Possibly huge amount of ‘threads’
    In the previous thought-experiment we ended up considering up to 10 million threads
    Best possible scaling is predicted to be reached when using 10000 threads (for 1 second worth of work)
Several problems
  Impossible to work with that many kernel threads (p-threads)
  Impossible to reason about this amount of tasks
  Requires abstraction mechanism

## Slide 58
Chart: Execution Time over Grainsize (Amount of work per Task)
| 160 | 320 | 640 | 1000 | 1250 | 1280 | 1600 | 2000 | 2500 | 3125 | 3200 | 4000 | 5000 | 6250 | 6400 | 8000 | 10000 | 12500 | 15625 | 16000 | 20000 | 25000 | 31250 | 32000 | 40000 | 50000 | 62500 | 78125 | 80000 | 100000 | 125000 | 156250 | 160000 | 200000 | 250000 | 312500 | 390625 | 400000 | 500000 | 625000 | 781250 | 800000 | 1000000 | 1250000 | 1562500 | 2000000 | 2500000 | 3125000 | 6250000 | 12500000 | 25000000 | 50000000 | 100000000
Sequential Time | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Time (16 Cores) | 16.6568 | 8.3558 | 4.2798 | 2.8252 | 2.3214 | 2.2513 | 1.8527 | 1.5797 | 1.2763 | 1.0778 | 1.053 | 0.90281 | 0.79028 | 0.72359 | 0.69586 | 0.65082 | 0.60003 | 0.46239 | 0.47898 | 0.47645 | 0.39048 | 0.38731 | 0.39298 | 0.39186 | 0.40287 | 0.4181 | 0.42323 | 0.44546 | 0.44553 | 0.46558 | 0.48758 | 0.50841 | 0.50618 | 0.52491 | 0.52785 | 0.53714 | 0.53686 | 0.53612 | 0.53559 | 0.54297 | 0.53475 | 0.53376 | 0.53543 | 0.53976 | 0.53195 | 0.52941 | 0.52473 | 0.532 | 0.53457 | 0.61202 | 0.65239 | 0.80501 | 1.3617
Static chunks | 0 | 16.6568

## Slide 59
Chart: Execution Time over Grainsize (Amount of work per Task)
| 160 | 320 | 640 | 1000 | 1250 | 1280 | 1600 | 2000 | 2500 | 3125 | 3200 | 4000 | 5000 | 6250 | 6400 | 8000 | 10000 | 12500 | 15625 | 16000 | 20000 | 25000 | 31250 | 32000 | 40000 | 50000 | 62500 | 78125 | 80000 | 100000 | 125000 | 156250 | 160000 | 200000 | 250000 | 312500 | 390625 | 400000 | 500000 | 625000 | 781250 | 800000 | 1000000 | 1250000 | 1562500 | 2000000 | 2500000 | 3125000 | 6250000 | 12500000 | 25000000 | 50000000 | 100000000
Sequential Time | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Time (16 Cores) | 16.6568 | 8.3558 | 4.2798 | 2.8252 | 2.3214 | 2.2513 | 1.8527 | 1.5797 | 1.2763 | 1.0778 | 1.053 | 0.90281 | 0.79028 | 0.72359 | 0.69586 | 0.65082 | 0.60003 | 0.46239 | 0.47898 | 0.47645 | 0.39048 | 0.38731 | 0.39298 | 0.39186 | 0.40287 | 0.4181 | 0.42323 | 0.44546 | 0.44553 | 0.46558 | 0.48758 | 0.50841 | 0.50618 | 0.52491 | 0.52785 | 0.53714 | 0.53686 | 0.53612 | 0.53559 | 0.54297 | 0.53475 | 0.53376 | 0.53543 | 0.53976 | 0.53195 | 0.52941 | 0.52473 | 0.532 | 0.53457 | 0.61202 | 0.65239 | 0.80501 | 1.3617
Static chunks | 0 | 16.6568

## Slide 60: Rule 3
Allow for your Grainsize to be Variable

## Slide 62: Efficiency Metrics
Efficiency(N) = Speedup(N)/ N = TS/(N * TP)
  Processor efficiency: figure of merit that indicates how well a parallel program uses available processors
  For ideal executions without overhead, 1/N <= Efficiency(N) <= 1
Half-performance metric
  : input size that achieves Efficiency(N) = 0.5 for a given
  Figure of merit that indicates how large an input size is needed to obtain efficient parallelism
  A larger value of indicates that the problem is harder to parallelize efficiently

## Slide 63: Complexity Measures
We'll say that a cost function is “order ”, or simply “”, read as “Big-O of ”
  Cost-X(n) < * f (n), for sufficiently large n, for some constant
Examples:

## Slide 64: Famous Complexity Classes
constant-time (head, tail)
logarithmic (binary search)
linear (vector multiplication)
"n logn" (sorting)
quadratic (matrix addition)
cubic (matrix multiplication)
polynomial (…many! …)
exponential (guess password)

## Slide 65: Complexity Measures
Focus on key metric of interest in your algorithm
Don’t count operations that are incidental to your algorithm
  They can be important implementation considerations, but may not contribute to understanding your algorithm
Since big-O analysis does not care about differences within a constant factor, you can just use a unit cost as a stand-in for a constant number of operations