## Slide 1: File Systems 1: Storage Devices and FAT
Lecture 16
Hartmut Kaiser
https://teaching.hkaiser.org/spring2026/csc4103/

## Slide 2: What’s a Bus?
Common set of wires for communication among hardware devices plus protocols for carrying out data transfer transactions
  Operations: e.g., Read, Write
  Control lines, Address lines, Data lines
Protocol: initiator requests access, arbitration to grant, identification of recipient, handshake to convey address, length, data
Very high BW close to processor (wide, fast, and inflexible), low BW with high flexibility out in I/O subsystem

## Slide 3: Typical PCI Architecture
CPU
RAM
Memory
Bus
USB Controller
SATA Controller
Scanner
Hard Disk
DVD ROM
Root Hub
Hub
Webcam
Mouse
Keyboard
PCI #1
PCI #0
PCI Bridge
PCI Slots
Host Bridge
ISA Bridge
ISA Controller
Legacy Devices
PCI: Peripheral Component Interconnect
ISA: Industry Standard Architecture
SATA: Serial AT Attachment

## Slide 4: How does the Processor Talk to the Device?
CPU interacts with a Controller
  Contains a set of registers that can be read and written
  May contain memory for request queues, etc.
Processor accesses registers in two ways:
  Port-Mapped I/O: in/out instructions
    Example from the Intel architecture: out 0x21,AL
  Memory-mapped I/O: load/store instructions
    Registers/memory appear in physical address space
    I/O accomplished with load and store instructions
Device
Controller
read
write
control
status
Addressable
Memory
and/or
Queues
Registers
(port 0x20)
Hardware
Controller
Memory Mapped
Region: 0x8f008020
Bus
Interface
Address +
Data
Interrupt Request
Processor Memory Bus
CPU
Regular
Memory
Interrupt
Controller
Bus
Adaptor
Bus
Adaptor
Other Devices
or Buses

## Slide 5: Memory-Mapped Display Controller
Memory-Mapped:
  Hardware maps control registers and display memory into physical address space
    Addresses set by HW jumpers or at boot time
  Simply writing to display memory (also called the “frame buffer”) changes image on screen
    Addr: 0x8000F000 — 0x8000FFFF
  Writing graphics description to cmd queue
    Say enter a set of triangles describing some scene
    Addr: 0x80010000 — 0x8001FFFF
  Writing to the command register may cause on-board graphics hardware to do something
    Say render the above scene
    Addr: 0x0007F004
Can be protected with address translation
Display
Memory
0x8000F000
0x80010000
Physical
Address
Space
Status
0x0007F000
Command
0x0007F004
Graphics
Command
Queue
0x80020000

## Slide 6: There’s more than just a CPU in there!

## Slide 7: Chip-Scale Features of Skylake (x86 in 2015)
Significant pieces:
  Four OOO (out-of-order) cores with deeper buffers
  Integrated GPU, System Agent (Mem, Fast I/O)
  Large shared L3 cache with on-chip ring bus
    2 MB/core instead of 1.5 MB/core
    High-BW access to L3 Cache
Integrated I/O
  Integrated memory controller (IMC)
    Two independent channels of DRAM
  High-speed PCI-Express (for Graphics cards)
  Direct Media Interface (DMI) Connection to PCH (Platform Control Hub)

## Slide 8: Skylake I/O: Platform Controller Hub (PCH)
Platform Controller Hub
  Connected to processor with proprietary bus
    Direct Media Interface
Types of I/O on PCH:
  USB, Ethernet
  Thunderbolt 3
  Audio, BIOS support
  More PCI Express (lower speed than on Processor)
  SATA (for Disks)
Sky Lake
System Configuration

## Slide 9: Operational Parameters for I/O
Data granularity: Byte vs. Block
  Some devices provide single byte at a time (e.g., keyboard)
  Others provide whole blocks (e.g., disks, networks, etc.)
Access pattern: Sequential vs. Random
  Some devices must be accessed sequentially (e.g., tape)
  Others can be accessed “randomly” (e.g., disk, CD, etc.)
    Fixed overhead to start transfers
  Some devices require continual monitoring (polling)
  Others generate interrupts when they need service
Transfer Mechanism: Programmed I/O and DMA

## Slide 10: Transferring Data To/From Controller
Programmed I/O:
  Each byte transferred via processor in/out or load/store
  Pro: Simple hardware, easy to program
  Con: Consumes processor cycles proportional to data size
Direct Memory Access:
  Give controller access to memory bus
  Ask it to transfer data blocks to/from memory directly
Interaction with DMA controller
1
2
3

## Slide 11: Transferring Data To/From Controller
Programmed I/O:
  Each byte transferred via processor in/out or load/store
  Pro: Simple hardware, easy to program
  Con: Consumes processor cycles proportional to data size
Direct Memory Access:
  Give controller access to memory bus
  Ask it to transfer data blocks to/from memory directly
Interaction with DMA controller
4
5
6

## Slide 12: Aside: Linux Memory Details
Memory management in Linux considerably more complex than the examples we have been discussing
Memory Zones: physical memory categories
  ZONE_DMA: < 16MB memory, DMA-able on ISA bus
  ZONE_NORMAL: 16MB  896MB (mapped at 0xC0000000)
  ZONE_HIGHMEM: Everything else (> 896MB)
Each zone has 1 freelist, 2 LRU lists (Active/Inactive)
Many different types of allocations
  SLAB allocators, per-page allocators, mapped/unmapped
Many different types of allocated memory:
  Anonymous memory (not backed by a file, heap/stack)
  Mapped memory (backed by a file)
Allocation priorities
  Is blocking allowed/etc.

## Slide 13: Aside: Linux Virtual Memory Map
Kernel Addresses
Empty
Space
User Addresses
User
Addresses
Kernel Addresses
0x00000000
0xC0000000
0xFFFFFFFF
0x0000000000000000
0x00007FFFFFFFFFFF
0xFFFF800000000000
0xFFFFFFFFFFFFFFFF
3GB Total
128TB
1GB
128TB
896MB Physical
64 TB Physical
32-Bit Virtual Address Space
64-Bit Virtual Address Space
“Canonical Hole”

## Slide 14: I/O Device Notifying the OS
The OS needs to know when:
  The I/O device has completed an operation
  The I/O operation has encountered an error
I/O Interrupt: Device generates interrupt when it needs service
  Handles unpredictable events well, but high overhead
Polling: OS periodically checks device-specific status register
  Low overhead, but may waste cycles for infrequent or unpredictable I/O
Actual devices combine both polling and interrupts
  E.g., high-bandwidth network adapter

## Slide 15: Kernel Device Structure
The System Call Interface
Process
Management
Memory Management
Filesystems
Device Control
Networking
Architecture
Dependent
Code
Memory Manager
Device Control
Network Subsystem
File System Types
Block Devices
IF drivers
Concurrency, multitasking
Virtual memory
Files and dirs: the VFS
TTYs and device access
Connectivity

## Slide 16: Device Drivers
Device-specific code in the kernel that interacts directly with the device hardware
  Supports a standard, internal interface
  Same kernel I/O system can interact easily with different device drivers
  Special device-specific configuration supported with the ioctl() system call
Device Drivers typically divided into two pieces:
  Top half: accessed in call path from system calls
    implements a set of standard, cross-device calls like open(), close(), read(), write(), ioctl() This is the kernel’s interface to the device driver
    Top half will start I/O to device, may put thread to sleep until finished
  Bottom half: run as interrupt routine
    Gets input or transfers next block of output
    May wake sleeping threads if I/O now complete

## Slide 17: Recall: Life Cycle of an I/O Request
Device Driver
Top Half
Device Driver
Bottom Half
Device
Hardware
Kernel I/O
Subsystem
User
Program

## Slide 18: The Goal of the I/O Subsystem
Provide Uniform Interfaces, Despite Wide Range of Different Devices
  This code works on many different devices:
  FILE fd = fopen("/dev/something", "rw"); for (int i = 0; i < 10; i++) { fprintf(fd, "Count %d\n", i); } close(fd);
  Why? Because code that controls devices (“device driver”) implements standard interface
We will try to get a flavor for what is involved in actually controlling devices in rest of lecture
  Can only scratch surface!

## Slide 19: Want Standard Interface to Devices
Block Devices: e.g. disk drives, tape drives, DVD-ROM
  Access blocks of data
  Commands include open(), read(), write(), seek()
  Raw I/O or file-system access
  Memory-mapped file access possible
Character Devices: e.g. keyboards, mice, serial ports, some USB devices
  Single characters at a time
  May not be buffered like block devices
  Libraries layered on top allow line editing
Network Devices: e.g. Ethernet, Wireless, Bluetooth
  Different enough from block/character devices to have an extended interface
  Unix and Windows include socket interface
    Separates network protocol from network operation
    Includes select() functionality
  Usage: pipes, FIFOs, streams, queues, mailboxes

## Slide 20: How Does User Deal with I/O Timing?
Blocking Interface: “Wait”
  When request data (e.g. read syscall), put process to sleep until data is ready
  When write data (e.g. write syscall), put process to sleep until device is ready for data
Non-blocking Interface: “Don’t Wait”
  Returns quickly from read or write request with count of bytes successfully transferred
  Read may return nothing, write may write nothing
Asynchronous Interface: “Tell Me Later”
  When request data, take pointer to user’s buffer, return immediately; later kernel fills buffer and notifies user
  When send data, take pointer to user’s buffer, return immediately; later kernel takes data and notifies user

## Slide 21: Storage Devices

## Slide 22: Hard Disk Drives (HDDs)
Western Digital Drive
http://www.storagereview.com/guide/
IBM/Hitachi Microdrive
Read/Write Head
Side View
IBM Personal Computer/AT (1986)
  30 MB hard disk - $500
  30-40ms seek time
  0.7-1 MB/s (est.)

## Slide 23: The Amazing Magnetic Disk
Unit of Transfer: Sector
  Ring of sectors form a track
  Stack of tracks form a cylinder
  Heads position on cylinders
Disk Tracks ~ 1µm (micron) wide
  Wavelength of light is ~ 0.5µm
  Resolution of human eye: 50µm
  100K tracks on a typical 2.5” disk
Separated by unused guard regions
  Reduces likelihood neighboring tracks are corrupted during writes (still a small non-zero chance)

## Slide 24: The Amazing Magnetic Disk
Track length varies across disk
  Outside: More sectors per track, higher bandwidth
  Disk is organized into regions of tracks with same # of sectors/track
  Only outer half of radius is used
    Most of the disk area in the outer regions of the disk
Disks so big that some companies (like Google) reportedly only use part of disk for active data
  Rest is archival data

## Slide 25: Shingled Magnetic Recording (SMR)
Overlapping tracks yields greater density, capacity
Restrictions on writing, complex DSP for reading

## Slide 26: Magnetic Disks
Cylinders: all the tracks under the head at a given point on all surfaces
Read/write data is a three-stage process:
  Seek time: position the head/arm over the proper track
  Rotational latency: wait for desired sector to rotate under r/w head
  Transfer time: transfer a block of bits (sector) under r/w head
Sector
Track
Cylinder
Head
Platter
Software
Queue
(Device Driver)
Hardware
Controller
Media Time
(Seek+Rot+Xfer)
Request
Result
Disk Latency = Queueing Time + Controller time +
Seek Time + Rotation Time + Xfer Time

## Slide 27: Disk Performance Example
Assumptions:
  Ignoring queuing and controller times for now
  Avg seek time of 5ms,
  7200RPM  Time for rotation: 60000 (ms/min) / 7200(rev/min) ~= 8ms
  Transfer rate of 50MByte/s, block size of 4Kbyte  4096 bytes/50×106 (bytes/s) = 81.92 × 10-6 sec  0.082 ms for 1 sector
Read block from random place on disk:
  Seek (5ms) + Rot. Delay (4ms) + Transfer (0.082ms) = 9.082ms
  Approx. 9ms to fetch/put data: 4096 bytes/9.082×10-3 s  451KB/s
Read block from random place in same cylinder:
  Rot. Delay (4ms) + Transfer (0.082ms) = 4.082ms
  Approx. 4ms to fetch/put data: 4096 bytes/4.082×10-3 s  1.03MB/s
Read next block on same track:
  Transfer (0.082ms): 4096 bytes/0.082×10-3 s  50MB/sec
Key to using disk effectively (especially for file systems) is to minimize seek and rotational delays

## Slide 28: Lots of Intelligence in the Controller
Sectors contain sophisticated error correcting codes
  Disk head magnet has a field wider than track
  Hide corruptions due to neighboring track writes
Sector sparing
  Remap bad sectors transparently to spare sectors on the same surface
Slip sparing
  Remap all sectors (when there is a bad sector) to preserve sequential behavior
Track skewing
  Sector numbers offset from one track to the next, to allow for disk head movement for sequential ops

## Slide 29: Typical Numbers for Magnetic Disk
Parameter | Info/Range
Space/Density | Space: 14TB (Seagate), 8 platters, in 3½ inch form factor! Areal Density: ≥ 1 Terabit/square inch! (PMR, Helium, …)
Average Seek Time | Typically 4-6 milliseconds
Average Rotational Latency | Most laptop/desktop disks rotate at 3600-7200 RPM (16-8 ms/rotation). Server disks up to 15,000 RPM. Average latency is halfway around disk so 4-8 milliseconds
Controller Time | Depends on controller hardware
Transfer Time | Typically 50 to 250 MB/s. Depends on: Transfer size (usually a sector): 512B – 1KB per sector Rotation speed: 3600 RPM to 15000 RPM Recording density: bits per inch on a track Diameter: ranges from 1 in to 5.25 in
Cost | Used to drop by a factor of two every 1.5 years (or faster), now slowing down

## Slide 30: Hard Drive Prices over Time

## Slide 31: Example of Current HDDs
Seagate Exos X14 (2018)
  14 TB hard disk
    8 platters, 16 heads
    Helium filled: reduce friction and power
  4.16ms average seek time
  4096 byte physical sectors
  7200 RPMs
  6 Gbps SATA /12Gbps SAS interface
    261MB/s MAX transfer rate
    Cache size: 256MB
  Price: $615 (< $0.05/GB)
IBM Personal Computer/AT (1986)
  30 MB hard disk
  30-40ms seek time
  0.7-1 MB/s (est.)
  Price: $500 ($17K/GB, 340,000x more expensive !!)

## Slide 32: Solid State Disks (SSDs)
1995 – Replace rotating magnetic media with non-volatile memory (battery backed DRAM)
2009 – Use NAND Multi-Level Cell (2 or 3-bit/cell) flash memory
  Sector (4 KB page) addressable, but stores 4-64 “pages” per memory block
  Trapped electrons distinguish between 1 and 0
No moving parts (no rotate/seek motors)
  Eliminates seek and rotational delay (0.1-0.2ms access time)
  Very low power and lightweight
  Limited “write cycles”
Rapid advances in capacity and cost ever since!

## Slide 33: SSD Architecture – Reads
  Read 4 KB Page: ~25 usec
  No seek or rotational latency
  Transfer time: transfer a 4KB page
    SATA: 300-600MB/s => ~4 x103 b / 400 x 106 bps => 10 us
  Latency = Queuing Time + Controller time + Xfer Time
  Highest Bandwidth: Sequential OR Random reads
Host
Buffer
Manager
(software
Queue)
Flash
Memory
Controller
DRAM
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
SATA

## Slide 34: SSD Architecture – Writes
Writing data is complex! (~200μs – 1.7ms )
  Can only write to empty pages in a block
  Erasing a block takes ~1.5ms
  Controller maintains pool of empty blocks by coalescing used pages (read, erase, write), also reserves some % of capacity
Rule of thumb:
  writes 10x slower than reads
  erasure 10x slower than writes
https://en.wikipedia.org/wiki/Solid-state_drive

## Slide 35: SSD Architecture – Writes
SSDs provide same interface as HDDs to OS – read and write chunk (4KB) at a time
But can only overwrite data 256KB at a time!
Why not just erase and rewrite new version of entire 256KB block?
  Erasure is very slow (milliseconds)
  Each block has a finite lifetime, can only be erased and rewritten about 10K times
  Heavily used blocks likely to wear out quickly

## Slide 36: Solution – Two Systems Principles
Layer of Indirection
  Maintain a Flash Translation Layer (FTL) in SSD
  Map virtual block numbers (which OS uses) to physical page numbers (which flash mem. controller uses)
  Can now freely relocate data w/o OS knowing
Copy on Write
  Don’t overwrite a page when OS updates its data
  Instead, write new version in a free page
  Update FTL mapping to point to new location

## Slide 37: Flash Translation Layer
No need to erase and rewrite entire 256KB block when making small modifications
SSD controller can assign mappings to spread workload across pages
  Wear Levelling
What to do with old versions of pages?
  Garbage Collection in background
  Erase blocks with old pages, add to free list

## Slide 38: Some “Current” 3.5in SSDs
Seagate Nytro SSD: 15TB (2017)
  Dual 12Gb/s interface
  Seq reads 860MB/s
  Seq writes 920MB/s
  Random Reads (IOPS): 102K
  Random Writes (IOPS): 15K
  Price (Amazon): $6325 ($0.41/GB)
Nimbus SSD: 100TB (2019)
  Dual port: 12Gb/s interface
  Seq reads/writes: 500MB/s
  Random Read Ops (IOPS): 100K
  Unlimited writes for 5 years!
  Price: ~ $50K? ($0.50/GB)

## Slide 39: HDD vs. SSD Comparison
SSD prices drop much faster than HDD

## Slide 40: SSD Summary
Pros (vs. hard disk drives):
  Low latency, high throughput (eliminate seek/rotational delay)
  No moving parts:
    Very light weight, low power, silent, very shock insensitive
  Read at memory speeds (limited by controller and I/O bus)
Cons
  Small storage (0.1-0.5x disk)
  Hybrid alternative: combine small SSD with large HDD
  Asymmetric block write performance: read pg/erase/write pg
    Controller garbage collection (GC) algorithms have major effect on performance
  Limited drive lifetime
    1-10K writes/page for MLC NAND
    Avg failure rate is 6 years, life expectancy is 9–11 years
These are changing rapidly!

## Slide 41: A Bit of I/O Performance

## Slide 42: Recall: Times (s) and Rates (op/s)
Latency – time to complete a task
  Measured in units of time (s, ms, us, …, hours, years)
Response Time - time to initiate and operation and get its response
  Able to issue one that depends on the result
  Know that it is done (anti-dependence, resource usage)
Throughput or Bandwidth – rate at which tasks are performed
  Measured in units of things per unit time (ops/s, GLOP/s)
Performance???
  Operation time (4 mins to run a mile…)
  Rate (mph, mpg, …)

## Slide 43: Basic Performance Concepts
Response Time or Latency: Time to perform an operation(s)
Bandwidth or Throughput: Rate at which operations are performed (op/s)
  Files: MB/s, Networks: Mb/s, Arithmetic: GFLOP/s
Start up or “Overhead”: time to initiate an operation
Most I/O operations are roughly linear in b bytes
  Latency(b) = Overhead + b/TransferCapacity

## Slide 44: Example (Fast Network)
Consider a link () with startup cost
Latency:
Effective Bandwidth:
Half-power Bandwidth:
For this example, half-power bandwidth occurs at

## Slide 45: Example: 10 ms Startup Cost (e.g., Disk)
Half-power bandwidth at
Large startup cost can degrade effective bandwidth
Amortize it by performing I/O in larger blocks
  Half-power b = 1,250,000 bytes!

## Slide 46: What Determines Peak BW for I/O?
Bus Speed
  PCI-X: 1064 MB/s = 133 MHz x 64 bit (per lane)
  ULTRA WIDE SCSI: 40 MB/s
  Serial Attached SCSI & Serial ATA & IEEE 1394 (firewire): 1.6 Gb/s full duplex (200 MB/s)
  USB 3.0 – 5 Gb/s
  Thunderbolt 3 – 40 Gb/s
Device Transfer Bandwidth
  Rotational speed of disk
  Write / Read rate of NAND flash
  Signaling rate of network link
Whatever is the bottleneck in the path…

## Slide 47: Overall I/O performance
Performance of I/O subsystem
  Metrics: Response Time, Throughput
  Effective BW = transfer size / response time
  Contributing factors to latency:
    Software paths (can be loosely modeled by a queue)
    Hardware controller
    I/O device service time
Queuing behavior:
  Can lead to big increases of latency as utilization increases
Response Time = Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

## Slide 48: Recall: I/O and Storage Layers
High Level I/O
Low Level I/O
Syscall
File System
I/O Driver
Application / Service
Streams
File Descriptors
open(), read(), write(), close(), …
Files/Directories/Indexes
Commands and Data Transfers
Disks, Flash, Controllers, DMA
What we covered before
What we will
cover next…
What we just
covered…

## Slide 49: From Storage to File Systems
I/O API and
syscalls
Variable-Size Buffer
File System
Block
Logical Index, Typically 4 KB
Hardware Devices
Memory Address
HDD
Sector(s)
Physical Index,
512B or 4KB
SSD
Flash Trans. Layer
Phys. Block
Phys Index., 4KB
Sector(s)
Sector(s)
Erasure Page

## Slide 50: Building a File System
Classic OS situation
Take limited hardware interface (array of blocks) and provide a more convenient/useful interface with:
Naming: Find file by name, not block numbers
Organize file names with directories
Organization: Map files to blocks
Protection: Enforce access restrictions
Reliability: Keep files intact despite crashes, hardware failures, etc.

## Slide 51: Translation from User to System View
What happens if user says: “give me bytes 2 – 12?”
  Fetch block corresponding to those bytes
  Return just the correct portion of the block
What about writing bytes 2 – 12?
  Fetch block, modify relevant portion, write out block
Everything inside file system is in terms of whole-size blocks
  Actual disk I/O happens in blocks
  read/write smaller than block size needs to translate and buffer
File
System
File (Bytes)

## Slide 52: Disk Management
The disk is accessed as a linear array of sectors.
How to identify a sector?
  Physical position
    Sector is a vector [cylinder, surface, sector]
    Not used anymore
    OS/BIOS must deal with bad sectors
  Logical Block Addressing (LBA)
    Every sector has an integer address
    Controller translates from address to physical position
    Shields OS from disk structure

## Slide 53: What Does the File System Need?
Track free disk blocks
  Need to know where to put newly written data
Track which blocks contain data for which files
  Need to know where to read a file from
Track files in a directory
  Find list of file's blocks given its name
Where do we maintain all of this?
  Somewhere on disk

## Slide 54: Data Structures on Disk
Bit different than data structures in memory
Access a block at a time
  Can't efficiently read/write a single word
  Have to read/write full block containing it
  Ideally want sequential access patterns
Durability
  Ideally, file system is in meaningful state upon shutdown
  This obviously isn't always the case…

## Slide 55: Critical Factors in File System Design
(Hard) Disks Performance !!!
  Maximize sequential access, minimize seeks
Open before Read/Write
  Can perform protection checks and look up where the actual file resource are, in advance
Size is determined as they are used !!!
  Can write (or read zeros) to expand the file
  Start small and grow, need to make room
Organized into directories
  What data structure (on disk) for that?
Need to carefully allocate / free blocks
  Such that access remains efficient

## Slide 56: FAT: File Allocation Table
MS-DOS, 1977
Still widely used!

## Slide 57: FAT (File Allocation Table)
Assume (for now) we have a way to translate a path to a “file number”
  i.e., a directory structure
Disk Storage is a collection of Blocks
  Just hold file data (offset o = <B, x>)
Example: file_read 31, <2, x>
  Index into FAT with file number
  Follow linked list to block
  Read the block from disk into memory
File 31, Block 0
File 31, Block 1
File 31, Block 2
Disk Blocks
FAT
N-1:
0:
0:
N-1:
31:
File number
memory

## Slide 58: FAT (File Allocation Table)
File is a collection of disk blocks
FAT is linked list 1-1 with blocks
File number is index of root of block list for the file
File offset: block number and offset within block
Follow list to get block number
Unused blocks marked free
  Could require scan to find
  Or, could use a free list
File 31, Block 0
File 31, Block 1
File 31, Block 2
Disk Blocks
FAT
N-1:
0:
0:
N-1:
31:
File number
memory
free

## Slide 59: FAT (File Allocation Table)
Where is FAT stored?
  On disk
How to format a disk?
  Zero the blocks, mark FAT entries “free”
How to quick format a disk?
  Mark FAT entries “free”
Simple: can be implemented in device firmware
File 31, Block 0
File 31, Block 1
File 31, Block 2
Disk Blocks
FAT
N-1:
0:
0:
N-1:
31:
File 1 number
memory
free
File 31, Block 3
File 2 number

## Slide 60: How to get the File Number?
Look up in directory structure
A directory is a file containing <file_name : file_number> mappings
  File number could be a file or another directory
  Operating system stores the mapping in the directory in a format it interprets
  Each <file_name : file_number> mapping is called a directory entry
Process isn’t allowed to read the raw bytes of a directory
  The read function doesn’t work on a directory
  Instead, see readdir, which iterates over the map without revealing the raw bytes
Why shouldn’t the OS let processes read/write the bytes of a directory?

## Slide 61: FAT: Directories
A directory is a file containing <file_name: file_number> mappings
Free space for new entries
In FAT: file attributes are kept in directory (!!!)
Each directory a linked list of entries
Where do you find root directory (“/”)?

## Slide 62: FAT Directory Structure
How many disk accesses to resolve “/my/book/count”?
  Read in file header for root (fixed spot on disk)
  Read in first data block for root
    Table of file name/index pairs. Search linearly – ok since directories typically very small
  Read in file header for “my”
  Read in first data block for “my”; search for “book”
  Read in file header for “book”
  Read in first data block for “book”; search for “count”
  Read in file header for “count”
Current working directory: Per-address-space pointer to a directory used for resolving file names
  Allows user to specify relative filename instead of absolute path (say CWD=“/my/book” can resolve “count”)

## Slide 63: Many Huge FAT Security Holes!
FAT has no access rights
FAT has no header in the file blocks
Just gives an index into the FAT
  (file number = block number)

## Slide 64: Conclusion: I/O Devices
I/O Devices Types:
  Many different speeds (0.1 bytes/sec to GBytes/sec)
  Different Access Patterns:
    Block Devices, Character Devices, Network Devices
  Different Access Timing:
    Blocking, Non-blocking, Asynchronous
I/O Controllers: Hardware that controls actual device
  Processor Accesses through I/O instructions, load/store to special physical memory
Notification mechanisms
  Interrupts
  Polling: Report results through status register that processor looks at periodically
Device drivers interface to I/O devices
  Provide clean Read/Write interface to OS above
  Manipulate devices through PIO, DMA & interrupt handling
  Three types: block, character, and network

## Slide 65: Conclusion: Storage Devices
Disk Performance:
  Queuing time + Controller + Seek + Rotational + Transfer
  Rotational latency: on average ½ rotation
  Transfer time: spec of disk depends on rotation speed and bit storage density
Devices have complex interaction and performance characteristics
  Response time (Latency) = Queue + Overhead + Transfer
    Effective BW = BW * T/(S+T)
  HDD: Queuing time + controller + seek + rotation + transfer
  SDD: Queuing time + controller + transfer (erasure & wear)
Systems (e.g., file system) designed to optimize performance and reliability
  Relative to performance characteristics of underlying device
Bursts & High Utilization introduce queuing delays

## Slide 66: Conclusion: File Systems
File System:
  Transforms blocks into Files and Directories
  Optimize for size, access and usage patterns
  Maximize sequential access, allow efficient random access
  Projects the OS protection and security regime (UGO vs ACL)
Naming: translating from user-visible names to actual sys resources
  Directories provide naming for local file systems
  Linked or tree structure stored in files
Components: directory, index, storage blocks, free list
File Allocation Table (FAT) – simple and primitive
  I-number = FAT index, FAT 1-1 with disk blocks, file is singly-link list of FAT=Blocks, directory is essentially file of <name, index, attributes> at known location
  Linear search – for block, for i-number